## Slide 1
Introduction to Computing and Application
Lecture 3: Data manipulation, computer architecture, machine instruction, and communication with other devices.
Ibrahim Abdullahi
Nile University of Nigeria, Abuja
Faculty of Natural and Applied Science Department of Software Engineering
© Adopted from UAI
SEN 101

## Slide 2
Summary of last lecture
Information representation in computer and some operation on them.
  Text
  Images
  Sound
  Numeric
Memory of computer
  Main memory
  Mass storage (secondary storage)
  Measure of memory capacity
©
2

## Slide 3
Computer architecture
  A circuitry that control data manipulation inside a computer is called central processing unit (CPU) or merely refers to as processor of a computer.
Today’s processor
©
3
  Executes instructions of a computer program by performing;
  Basic Arithmetic
  Logical Operations
  Control Operations
  I/O Operations
    As specified by the instructions…

## Slide 4
CPU basics
CPU
Control unit
Registers
Arithmetic/logic
Operation on data
  Addition
  Subtraction
Coordinating activities
Buffer cells within CPU
GPR
SPR
©
4

## Slide 5
CPU basic
  General Purpose registers: is a buffer for data manipulated by CPU
    Holds input to the ALU circuitry.
    Provide storage space for the result of that (ALU) unit.
  The control unit transfer the data from main memory to GPR
    Tell the ALU which registers hold the data
    Activate the appropriate circuitry within the ALU, and
    Inform the ALU which register should receive the result.
©
5

## Slide 6: Computer Bus
Physical connections (cables, circuits etc.); hardware components that facilitate communication

## Slide 7
Bridge between CPU and main memory
Bus
©
7

## Slide 8
Addition operation on value stored in memory
Bus
©
8

## Slide 9
Cache memory
  A high speed memory located within the CPU that attempt to copy a portion of main memory that is of current interest. Data transfer that would be made between the register and main memory are made between the register and the cache memory. Any changes made to the cache are then transferred collectively to the main memory at a more opportune time.
©
9

## Slide 10
Stored-program concept
  Early computers generation everyone thought of programs and data as different entities:
    Data were stored in memory
    Programs were part of the CPU
  The idea of storing a computer’s program in its main memory is called the stored-program concept
© UAI
10

## Slide 11
Machine language
  To apply the stored-program concept, CPUs are designed to recognize instructions encoded as bit patterns. The collection of instruction expressed in this coding system is called machine language. An instruction expressed in this language is called machine-level instruction or, more commonly, a machine instruction
© UAI
11

## Slide 12
Data transfer instructions
  Machine instructions can be categorized into three groupings: data transfer, ALU, and control.
  Data transfer instructions that request the movement of data from one location to another.
    Terms used when referring to the transfer of data from the CPU and main memory. A request to fill the GPR with the content of main memory cell is referred to as a LOAD instruction. A request to transfer the content of the register to main memory is called STORE instruction.
    An important instruction within data transfer is called I/O instruction for communicating with devices outside the CPU.
© UAI
12

## Slide 13
ALU instructions
  Consist of instructions that tell the control unit to request an activity within the ALU.
  Operation of ALU
    Addition and Subtraction
    Performing Boolean operations (AND, OR and XOR)
© UAI
13

## Slide 14
Control instructions
  Consist of instructions that direct the execution of a program rather than the data manipulation. Step 3 in next slide falls into this category. The instruction term used in this section are JUMP (or BRANCH) instructions used to direct the CPU to execute an instruction other than the next one in the list.
© UAI
14

## Slide 15
Dividing value stored in memory
© UAI
15

## Slide 16
Communication with other device
Direct access memory
  "Direct Memory Access." DMA is a method of transferring data from the computer's RAM to another part of the computer without processing it using the CPU. ...
  For example, a sound card may need to access data stored in the computer's RAM, but since it can process the data itself, it may use DMA to bypass the CPU.
  Example, projector
Handshaking
  A situation in which the peripheral device also send information to the computer
    Example, printer
© UAI
16

## Slide 17
communication media
Parallel communication
  Data can be transmit via multiple path
Serial communication
  Data transmission using single path
Communication rate
  Depending on the medium (kb, mb, …)
© UAI
17

## Slide 18
Summary
Computer architecture
The CPU basics
  ALU
  Control unit
  Register unit
Machine instruction
  Data transfer
  ALU
  Control
Communication with other devices
  Direct access memory
  Handshaking
  Communication media
    Parallel communication
    Serial communication
  Communication rates
© UAI
18

## Slide 19
Glimpse of next class
OS
Types of OS
Type of computer software
Component of OS
Concept of process within a computer
© UAI
19

## Slide 20
Question????
Thank you for coming.
© UAI
20